## Slide 1: ZeroVM and ZVM Runtime (ZRT)
Ryan McKinney
Senior Software Engineer, Rackspace

## Slide 2: Agenda
ZeroVM
  What is ZeroVM?
  Architecture
  Guest Memory Layout
  Anatomy of a Syscall
ZeroVM Runtime (ZRT)
  Syscall handling (zcalls)
Code Review
  ZeroVM
  ZRT/ZVM-toolchain/ZeroVM interrelation

## Slide 3: “Left as an exercise for the reader.”
ZeroVM
  Manifests
    https://github.com/zerovm/zerovm/blob/master/doc/manifest.txt
  Channels
    https://github.com/zerovm/zerovm/blob/master/doc/channels.txt
ZRT full library review
  There’s a lot! (think glibc)
In-depth ZVM GCC toolchain architecture
  It’s complicated, and I don’t want to
Native Client (NaCl) assembly
  http://www.chromium.org/nativeclient/how-tos/how-to-write-assembler-for-x86-nacl-platform
GOOD LUCK!

## Slide 4: ZeroVM
What is it?

## Slide 5: The (sort of) Plain English Description
ZeroVM creates a secure isolated execution environment that allows users to run a single application or program.
Notes: specifically x86_64 segmentation
Adapting Software Fault Isolation to Contemporary CPU Architectures
https://www.usenix.org/legacy/event/sec10/tech/full_papers/Sehr.pdf

## Slide 6: Some Technical Details
Based on the Chromium Native Client (NaCl) project
Leverages ZeroMQ ZBroker (networked named pipes)
Includes a full compiler toolchain
ZRT provides a subset of the POSIX API
ZRT also includes a port of the CPython interpreter
Notes: Software Fault Isolation (SFI) sandbox
segment addressing

## Slide 7: ZeroVM
Architecture

## Slide 8: ZeroVM Architecture Overview

## Slide 9: ZeroVM Guest Memory Layout

## Slide 10: ZeroVM
Anatomy of a Syscall

## Slide 11: ZeroVM - Traps and Trampolines
Syscalls
  are the interface between untrusted and trusted codebase allowing limited and verified code execution outside of the sandbox
  start as a call from untrusted code to a trampoline (TrapHandler)
ZeroVM owns a trusted context as well as an untrusted context
  untrusted code cannot read the trusted stack, and trusted code can’t use the untrusted stack
  nothing can use the stack unless the appropriate context switch takes place
Dispatcher does the following:
  Determine which syscall was called
  Look up the syscall implementation in the dispatch table
  Call the syscall
  Initiate the context switch back to untrusted code

## Slide 12: ZeroVM – Anatomy of a Syscall
Notes: Blatantly ripped from Google Native Clients – Anatomy of a Syscall
http://www.chromium.org/nativeclient/reference/anatomy-of-a-sys

## Slide 13: ZeroVM - Traps and Trampolines
Defined in: zerovm/api/zvm.h
ZVM API – (i.e. Trap functions)
  TrapRead – read from channel
  TrapWrite – write to channel
  TrapExit – terminate the guest program
  TrapJail – validation of the memory block.
    if validation is successful the memory block will be marked as “read only” and “executable”
  TrapUnjail – memory block will be marked as “read/write”
  TrapFork – convert running zerovm to “daemon” mode.
    spawn new sessions via unix socket request
    new sessions will start from the address next after zvm_fork() call

## Slide 14: ZeroVM Runtime (ZRT)
syscall handling (zcalls)

## Slide 15: ZRT - syscalls
Syscalls
  read  zmv_pread
  write  zmv_pwrite
Non-Syscall Syscalls
  open  handled internally by ZRT within untrusted code
  close  handled internally by ZRT within untrusted code

## Slide 16
Exposes ZVM API by replacing the appropriate syscalls in glibc
  open
  close
  read
  write
ZeroVM Runtime (ZRT)
  Syscall handling (zcalls)
  ZVM-toolchain/ZRT/ZeroVM interrelation

## Slide 17: Questions?
Website: www.zerovm.org
Github: https://github.com/zerovm/
User Mailing List: zerovm@googlegroups.com
Development Mailing List: zerovm-devel@googlegroups.com
IRC: #zerovm on Freenode
Notes: http://www.chromium.org/nativeclient/reference/research-papers